2 dimensional 2 joint inverse kinematics
problem: f(x,y,d1,d2) = Ө2, then derive Ө1
servo1: origin=(0,0), length=d1, angle=Ө1, servo 2: length=d2 angle Ө2

Ө2 = acos((x2+y2-d12-d22)/(2*d1*d2))	solution set +/- Ө2 +2kπ
Ө1 = atan(y/x)-asin(d2*sinӨ2/sqrt(x2+y2)) solution set Ө1 +kπ*

Implementing computation:
exclude divison by zero (when x=0, atan of infinity is pi/2)
use the correct solution (x>0 use second solution in the set ie. Ө1+π

2.5 joint 3 dimensional inverse kinematics

problem: f(x,y,z,d1,d2) = Ө2, then derive Ө1 , Ө3
servo0:origin(0,0),length=0, angle=Ө3, rotates around x axis
servo1:origin=(0,0), length=d1, angle=Ө1,, rotates in y'x plane
servo 2: length=d2 angle Ө2, ,, rotates in y'x plane

Ө3= atan(z/y) solution set Ө3+ kπ/2
use 2d plane y'*x and from 2d equations above derive Ө2 and Ө1
y'=sqrt( y2 +z2) now substituting y' for y
Ө2 = acos((x2+y2+z2-d12-d22)/(2*d1*d2))	solution set +/- Ө2 +2kπ
Ө1 = atan(y'/x)-asin(d2*sinӨ2/sqrt(x2+y2+z2)) solution set Ө1 +kπ*

Forward Kinematics Now calculate which solutions hold true for our model, using forward kinematics.
2 dimensions, 2 joints: / x = d1*cos Ө1 + d2*cos Ө1+Ө2 / y = d1*sin Ө1 + d2*sin Ө1+Ө2	3 dimensions, 2.5 joints: / x = d1*cos Ө1 + d2*cos Ө1+Ө2, / y' = d1*sin Ө1 + d2*sin Ө1+Ө2 / y = y' cos Ө3, / z = -y' sin Ө3

So final algorithm

Walking gaits in quadrupeds

Rotation of quadrupeds